## Slide 1: 基於智慧空間之銀髮族日常生活活動觀測照護系統 Activity of Daily Living-aware Elderly Health in Pervasive Environment
研究生：陳雅虹
指導教授：傅立成老師
Intelligent Robot and Automation Lab Department of Computer Science and Information Engineering National Taiwan University
Notes: 老爹：有點黑，不太好XD

## Slide 2: Outline
Introduction
Activity Recognition
Activity of Daily Living-aware Elderly Healthcare
Evaluation
Conclusion and Future Work

## Slide 3: Aging Population
World’s population has become older
  Population aging
    The shift of a country’s median age toward elder age
  Prediction of world’s median age
    2000：26.6 years
    2050：37.3 years
    2100：45.6 years
Aged population in Japan

## Slide 4: Aging in Place
The ability to live in one’s own home and community safely, independently, and comfortably, regardless of age, income, or ability level
The risks the elders are facing still exist
  Fall
  Loss of autonomy
  Dementia symptoms

## Slide 5: Activity of Daily Living
Activity of daily living is an important factor to estimate the independent ability of elders
Monitoring the ADL of elders to measure their ability can improve the safe living conditions at home

## Slide 6: Motivation
Realizing activity of daily living is an important role for elderly care
The scarcity of medical resource
  Remote healthcare and vital-sign monitoring system are explored
Most elder people tend to live their own house
  35% of those live at care home could be potentially supported at home

## Slide 7: Motivation
Wireless sensor network (WSN) is a well-developed technology in recent years
  e.g. mobile pad, smart watch or raspberry Pi with ambient sensors
Based on mature of WSN, the technologies of automatic monitoring activity are proposed in the experimental stage
  Both ambient Intelligent and mobile computing develops the technique of activity recognition
  It is hard to identify the activity without mapping sesnosrs

## Slide 8: Objective
To propose a system that helps caregivers monitor elders’ ADL in their home
  Monitoring elders activity in real-time
  Training activity recognition model with lower efforts
  Adaptive learning new lifestyle by discovering unknown activity

## Slide 9: Challenge
Integrating ambient sensor and body sensor network
  The methods of data analysis between Ambient Intelligent (AmI) and mobile computing are different
High cost on labeling activity
  Ground truth of each instance in machine learning are necessary
Adaptive learning of activity recognition
  With aging, elderly people may have new lifestyles

## Slide 10: Related Work
Discovery of Human Activity | Sensor Network |  | Nonparametric Learning | Discovery Unknown Activity
 | BSN | ASN |  | 
The proposed Model | ✓ | ✓ | ✓ | ✓
Sun et al. [1] | ✓ |  | ✓ | 
Yuan et al. [2] | ✓ |  |  | ✓
Cheng et al. [3] | ✓ |  | ▲ | ✓
Sanchez et al. [4] |  | ✓ |  | 
Cook et al. [5] |  | ✓ | ▲ | ✓
Zhang et al. [6] |  | ✓ |  | 
▲: the learning methods use less effort to build their models, but they are not nonparametric learning. |  |  |  | 
[1] F.-T. Sun, Y.-T. Yeh, H.-T. Cheng, C. Kuo, and M. Griss, "Nonparametric discovery of human routines from sensor data," in Pervasive Computing and Communications (PerCom), 2014 IEEE International Conference on, 2014, pp. 11-19.
[2] B. Yuan and J. Herbert, "Context-aware hybrid reasoning framework for pervasive healthcare," Personal and ubiquitous computing, vol. 18, pp. 865-881, 2014.
[3] H.-T. Cheng, M. Griss, P. Davis, J. Li, and D. You, "Towards zero-shot learning for human activity recognition using semantic attribute sequence model," in Proceedings of the 2013 ACM international joint conference on Pervasive and ubiquitous computing, 2013, pp. 355-358.
[4] D. Sanchez, M. Tentori, and J. Favela, “Hidden markov models for activity recognition in ambient intelligence environments,” in [5] Current Trends in Computer Science, 2007. ENC 2007. Eighth Mexican International Conference on, 2007, pp. 33-40.
D. J. Cook, N. C. Krishnan, and P. Rashidi, "Activity discovery and activity recognition: A new partnership," Cybernetics, IEEE Transactions on, vol. 43, pp. 820-828, 2013.
[6] Q. Zhang, M. Karunanithi, R. Rana, and J. Liu, "Determination of Activities of Daily Living of independent living older people using environmentally placed sensors," in Engineering in Medicine and Biology Society (EMBC), 2013 35th Annual International Conference of the IEEE, 2013, pp. 7044-7047.

## Slide 11: System Overview
Training Mode
Online Mode

## Slide 12: Outline
Introduction
Activity Recognition
Activity of Daily Living-aware Elderly Healthcare
Evaluation
Conclusion and Future Work

## Slide 13: Architecture of Activity Recognition Model
An activity recognition model is proposed to real-time monitor elderly residents’ activity of daily living
To achieve lower efforts on labeling, the model has two modes
Training mode
  Trying to categories data in order to reduce the number of labeling data
Online mode
  Real-time monitoring elders’ activity
  Discovering unknown activity

## Slide 14: Describing Parts
Training Mode
Online Mode

## Slide 15: Activity Recognition of Training Mode
The AR model of training mode has two main layer
First layer contains two separated AR models for ambient and vital sign data
  A KNN model for ambient data
  A topic model DPMM for vital sign data
Second layer integrates the results from ambient and vital sign and builds the AR model
Training data are categorized by the AR model of training mode
  Users only need to label each category

## Slide 16: Activity Recognition of Training Mode
To achieve lower efforts on labeling, the AR model in training mode should not require prior knowledge
  Supervised learning needs to give ground truths on data
  Some unsupervised learning requires prior knowledge, e.g., K-means should gives a specific number k
Non-parametric methodologies are necessary to build the AR model
The proposed activity recognition model is a non-parametric hierarchical activity recognition model (NHARM)

## Slide 17: Activity Recognition of Ambient Part
We are monitoring environment state by current sensors, lumen sensor and switch sensors
Because ambient sensors are triggered by human activity, their data extracts as Boolean variable
If a value of input sensor data is higher than the threshold T, the activity status of its appliance is “On”; otherwise it is “Off”.
Current Sensor
Lumen Sensor

## Slide 18: Activity Recognition of Ambient Part
Using k-nearest neighbor (KNN) to build the activity recognition model
Before building model, deciding cluster heads is necessary
The cluster head is decided by time-frequency (TF) of instances
  If an instance’ TF is higher than 1%, we regard this case as one of cluster head
The features’ dimension is the number of sensors m

## Slide 19: Activity Recognition of Ambient Part
Let be the training set, where
The similarity measurement uses Manhattan distance
The identity function
  Where is the cluster head for ith neighbor of
The number of neighbors with cluster

## Slide 20: Activity Recognition of Ambient Part
The function of weight voting is used to determine one instance belongs to which cluster
The instance will belong to the closet cluster

## Slide 21: Activity Recognition of Vital Sign Part
A wearable device “Zen watch” is used to monitor human’s behavior
  The sensors on Zen watch are accelerometer and gyroscope
The behavior of human can be categorized to two types: static and dynamic behaviors
  We consider each are “posture” and “motion”
  Posture: hand is usually turning in a fixed direction
  Motion: hand is always moving but not turning in a fixed direction
Reading
Sweeping
Posture
Motion

## Slide 22: Activity Recognition of Vital Sign Part
To detect posture and motion actions by monitoring the device’s orientation and acceleration variable
  Orientation captures from accelerometer and gyro
  Condensing the raw data as mean or variance
Orientation helps to detect “Posture” action
Acceleration helps to detect “Motion” action
Orientations | Accelerations
Mean of Pitch | Mean of each axis
Mean of Roll | Variance of each axis
Angle variation of Pitch | Signal vector magnitude
Angle variation of Roll | 

## Slide 23: Activity Recognition of Vital Sign Part
Patterns of wearable sensor data
  Each feature inside the wrist watch indicates a waving action
  Numbers of consecutive waving motions can be associated with a specific activity
A topic model is proposed to infer one minute behavior
  It can automatically extract activity patterns from sensor data
  Taking each feature collected every second as “word” and 11 words construct a vocabulary
  A sequence of vocabularies represents one topic
  An activity is considered as one document which has its topic
  A waving motion is considered as one waving motion

## Slide 24: Activity Recognition of Vital Sign Part
The topic model is constructed by two layers Dirichlet process mixture model (2LDPMM)
2LDPMM is a non-parametric unsupervised learning inference model
  It’s hard to define the specific number of kinds of hand’s waving motions
  2LDPMM is a data-driven method, so it can find different kinds of hand’s waving motion from raw data without given a specific number

## Slide 25: Activity Recognition of Vital Sign Part
The topic model is constructed by two layers Dirichlet process mixture model (2LDPMM)
  First Layer recognizes waving motion
  Second Layer recognizes activity by concatenating 60 successive waving motions
2LDPMM is a non-parametric unsupervised learning inference model
  It’s hard to define the specific number of kinds of hand’s waving motions
  2LDPMM is a data-driven method, so it can find different kinds of hand’s waving motion from raw data without given a specific number

## Slide 26: Dirichlet Process Mixture Model
Dirichlet distribution is the conjugate prior of multinomial distribution
Binomial distribution
Multinomial distribution
  Where , and

## Slide 27: Dirichlet Process Mixture Model
Dirichlet distribution is the conjugate prior of multinomial distribution
  Where and
Two parameters
  Concentration
  Base measure that

## Slide 28: Dirichlet Process Mixture Model
Dirichlet process (DP) is an infinite-dimensional generalization of Dirichlet distribution
DP also has two parameters
  Strength likes an inverse-variance of DP
  Base distribution likes the mean of DP
If for any partition of :

## Slide 29: Dirichlet Process Mixture Model
DPMM generalizes finite mixture models
  The number of mixture components can be infinite
Using the Dirichlet distribution to construct a finite mixture model
  A data point is drawn from the mixture model
for

## Slide 30: Dirichlet Process Mixture Model
Using the Dirichlet process to construct an infinite mixture model
  In other words, let
  The mixture model becomes

## Slide 31: Activity Recognition of Vital Sign Part
In the dataset of vital sign data, both topics and vocabularies have the Dirichlet prior
2LDPMM recognizes vocabulary in first layer and recognizes topic in second layer
  Concatenating 60 successive vocabularies as one document
Chart: Having Meal
 | 14 | 11 | 8 | 21 | 5 | 1
Chart: Reading
 | 32 | 5 | 17 | 2 | 4 | 0
Chart: Sweeping
 | 2 | 7 | 2 | 9 | 4 | 36
The occurrence time of different vocabularies in four topics
Chart: Watching TV
 | 29 | 19 | 5 | 4 | 3 | 0

## Slide 32: AR model of Ambient and Vital Sign Fusion
Fusing ambient and vital sign information to detect more precise living activity
  Considering each cluster of 2LDPMM is a sensor
  Each sensor is used to sensing a specific activity
We can snapshot sensors’ active status from both ambient and vital sign sensors in the same time
  Each cluster of second layer clustering result means one living activity
  User can only label those clusters
  Reducing the high burden on labeling data

## Slide 33: AR model of Ambient and Vital Sign Fusion
Using k-nearest neighbor (KNN) to build second layer activity recognition model
Based on the results of first layer, we can find time frequency (TF) of both ambient and vital sign instances
The cluster head is also decided by TF
  If an instance’ TF is higher than 1%, we regard this case as one of cluster head
The dimension space is
  is the number of types of waving motions
  is the number of ambient sensors

## Slide 34: AR model of Ambient and Vital Sign Fusion
Feature extraction from first layer model
  The concatenating waving motions from vital sign AR model
  An accumulated results from ambient AR model for 1 minute
Accumulated results from ambient model
TF of waving motions from vital sign model

## Slide 35: Activity Recognition Model of Online Mode
Using Hidden Markov Model (HMM) to build online mode AR model
  Because user can label data in training mode, the online mode uses an supervised learning method
Hidden Markov Model determines activity using the instance’s observations and the previous state
  The training mode is regardless temporal information

## Slide 36: Activity Recognition Model of Online Mode
The features of HMM is same to the second layer non-parametric hierarchical activity recognition model
Let sequential data , and
  Every is generated by a hidden state where
The detail implementation of HMM describes in [1]
[1] P. Blunsom, "Hidden markov models," Lecture notes, vol. 15, pp. 18-19, 2004.

## Slide 37: Outline
Introduction
Activity Recognition
Activity of Daily Living-aware Elderly Healthcare
Evaluation
Conclusion and Future Work

## Slide 38: Activity of Daily Living-aware System
The healthcare system can real-time aware residents’ activity based on proposed activity recognition models
Three main components of activity-aware system
  The function of activity recognition
  The interface of labeling data
  The function of discovering unknown activity
Notes: The methods of activity recognition have been described in previous slides

## Slide 39: Describing Parts
Training Mode
Online Mode

## Slide 40: The Interface of Labeling Data
After building NHARM in training mode, training data are categorized into clusters
  Each cluster represents an living activity
  Labeling all clusters to regenerate training data with label
A GUI is designed for user labeling clusters

## Slide 41: The Interface of Labeling Data
According to the timeline presented information
  Each color represents a cluster
  A set of living activities integrated into a list, so user can choose cluster’s activity by the list
After labeling them, generating the new dataset

## Slide 42: The Interface of Labeling Data
We also ask users to note the emergency level for all activities
  If an activity belongs to abnormal, once detecting this activity sends alert message to user’s caregiver
  If an activity belongs to normal, the system does nothing

## Slide 43: Adaptive Learning on Online Mode
To achieve the function of discovering unknown activity, adaptive learning is necessary for AR model
We design a similarity function for detecting whether the input instance is known activity or not
  The similarity function calculates the similarity scores of all activities
  If the highest score is lower than threshold T, this input instance may be an unknown activity

## Slide 44: Adaptive Learning on Online Mode
If discovering an unknown activity, the mechanism of adaptive learning is triggered
  The adaptive learning is built by case-based reasoning (CBR)
CBR is the process of solving new problems based on the solutions of similar past problems
  So the system provides a service of the most similar activity

## Slide 45: Adaptive Learning on Online Mode
After proving service immediately, the system will require user or caregiver to confirm this instance
According to the confirm information, re-train the activity recognition model of HMM

## Slide 46: Adaptive Learning on Online Mode
A case-based reasoning measurement is denoted as
  is denoted as a set of input description for which a service
  is in the case base
A similarity function is mapping to
  Where is the Manhattan distance of feature i

## Slide 47: Outline
Introduction
Activity Recognition
Activity of Daily Living-aware Elderly Healthcare
Evaluation
Conclusion and Future Work

## Slide 48: Outline
Introduction
Activity Recognition
Activity of Daily Living-aware Elderly Healthcare
Evaluation
Conclusion and Future Work

## Slide 49: Conclusion
We have proposed a healthcare system to monitor the activities of daily living for elders in their home environments.
The activity monitoring model is more appropriate for real living environment
  A better performance of activity recognition by fusing sensors
  Reducing the burden on labeling stage
  It is able to discovery unseen activity automatically and retraining the AR model

## Slide 50: Future works
A more friendly interface for elderly user
  We can invite some elderly people use our system and give some feedbacks
  Base on those feedbacks to improve the labeling interface
Developing more applications based on the activity-aware system
  The service is simple that we only give alert message when the system monitors the abnormal activity labeled by user
  There are more useful applications can imply in the our healthcare system based on the real-time monitoring activity